## Slide 1: LTE sidelink enhancements
Notes: 這邊的enhancement包含了 提高QoS, 更高的效率、可靠性，降低複雜度、電力等

## Slide 2: General considerations on sidelink enhancements
On bandwidth capabilities of evolved ProSe UE-to-Network Relay UE and evolved ProSe Remote UEs:
  Evolved ProSe UE-to-Network Relay UEs support all DL/UL/SL system bandwidth capabilities
  BW limitations are supported for evolved ProSe Remote UEs;
Notes: 這邊在談論的是UE的bandwidth capabilities
Relay UE必須擁有Downlink, Uplink , SideLink的頻寬
Remote UE 支持 BW限制

## Slide 3
On UEs with 1 PRB bandwidth:
For Remote UEs with 1 PRB bandwidth limitation new SLSS/PSBCH format is needed.
  PSBCH/SLSS bandwidth is one PRB;
  New PSBCH format includes the legacy PSBCH content.
  NOTE: for UEs w/o sidelink reception capabilities new SLSS/PSBCH format is not needed
Notes: 這邊在討論當頻寬限制是1PRB的時候，需要有新的SLSS/PSBCH 的格式，
然後這邊規範新的format，PSBCH / SLSS的頻寬要是 1 PRB
並且可以兼容舊的PSBCH格式
但是若UE沒有sidelink的接收功能就不需要有新的SLSS /PSBCH格式了。
PRB是排程的最小資源單位，1PRB有12個連續子載波

## Slide 4
The following is assumed for further design of sidelink communication, synchronization, and discovery for 1 PRB bandwidth limited UEs
  SC-FDMA waveform can be used for sidelink transmission and reception;
  TBCC can be used as a channel coding scheme for all sidelink physical channels;
  Support of sub-PRB and 3.75 kHz subcarrier spacing sidelink transmission/reception is deprioritized.
  For Remote UEs with 1 PRB bandwidth limitation new PSDCH format is needed
Notes: 這邊都是假設頻寬限制是 1 PRB下 來討論sidelink中的communication, synchronization, discovery:
SC – FDMA波型 要可以接收跟發送資料
TBCC (Tail-biting convolution code)要可以成為sidelink physical channels 的channel coding scheme
不需要優先支持Sub- PRB and 3.75kHz subcarrier spacing 在sidelink 的發送跟接收
因remote ue在 1 PRB 的頻寬限制下，因此必須有新的PSDCH格式

## Slide 5
The following discovery design options are identified for UEs with 1 PRB BW limitation
  Option 1: Define 1 PRB / 1 TTI physical structure and reduce payload size;
  Option 2: Define 1 PRB / 2 TTIs physical structure and keep the same payload size;
  Option 3: Define 1 PRB / 1 TTI physical structure and increase modulation order (e.g. to 16-QAM);
  Other options are not precluded
Notes: 那這邊有三種可考慮的設計選項作為sidelink 的discovery 當UE頻寬為1PRB的時候:
第一個就是要定義 1 PRB 或 1TTI 的physical structure 並縮小payload大小，
第二個就是要定義 1 PRB 或 2TTI 的physical structure 維持payload 大小
第三個就是要定義 1 PRB 或 1TTL 的physical structure但增加調變的order

## Slide 6: At least the following sidelink enhancements for UEs with 6 PRB bandwidth limitation can be applicable for UEs with 1 PRB bandwidth limitations;
- eNB controlled and Relay UE assisted resource allocation modes;
- Sidelink SPS;
- Sidelink power control;
- Sidelink feedback;
- Sidelink measurements.
Notes: 原本6PRB頻寬限制下的UE若變為1PRB 的話，以下的項目都能夠增強。
eNB控制和relay UE輔助的資源分配模式
Sidelink 半永久的排程方式
Sidelink power control;
Sidelink feedback;
Sidelink measurements.

## Slide 7: At least the following additional work is needed to support 1 PRB UEs
- Additional consideration on PSCCH/PSSCH resource pool configuration;
- Restriction of TBS size and/or TTI bundling aspects for sidelink communication;
- Sidelink measurement accuracy.
Notes: 那要實現1PRB限制的話，還要額外考慮以下幾項:
有關PSCCH / PSSCH資源池配置的其他注意事項
TBS(Transport Block Size)的限制大小以及TTI bundle方面的sidelink通訊(TTI bundling是在多个连续的subframe上多次发送同一个TB（Transport Block），而无需等待ACK/NACK的技术，目的就是为了提高cell边缘UE的上行覆盖)
Sidelink 的測量精度

## Slide 8: On semi-persistent transmission:
Semi-persistent transmission (e.g. similar to SPS) over sidelink is considered useful
  eNB schedules sidelink SPS via evolved ProSe UE-to-Network Relay UE forwarding for the evolved ProSe Remote UE linked with the relay UE;
  eNB schedules sidelink SPS for the evolved ProSe Remote UE linked with the evolved ProSe UE-to-Network Relay UE;
  Relay UE schedules sidelink SPS for the evolved ProSe Remote UE linked with the evolved ProSe UE-to-Network Relay UE.
Notes: 若是採用semi-persistent transmission的話，以下都可能會被強化
eNodeB 排程 UE-to-Network UE forward到有relay UE連著的remote ue
Relay ue 排程 UE-to-Network UE 連到remote ue
以往的Mobile Network的封包傳輸，都是使用Dynamic Scheduling，也就是要傳輸的時候，才開始要空中資源，一般上行的資料都是用Random access的方式，而下行都是用Paging的方式。但因為未來在LTE上必須乘載Voice的訊息，對於Voice來說，若使用Dynamic Scheduling的方式並不適合，因為此種方式會在通話期間會一直持續要資源，並且Voice本身的traffic不大，反而會造成control channel的負擔。
使用Semi-Persistent Scheduling(SPS)是來分配persistent PRB，沒有Voice traffic 就自動釋放PRB，等到有Voice traffic則再次請求persistent PRB，這樣即可省下大量在Schduling control的資源。